## Slide 1
Evolution of CMOS device and technology for low power applications
Dr. Sanatan Chattopadhyay
Department of Electronic Science

Centre for Research in Nanoscience and Nanotechnology
University of Calcutta

## Slide 2
Systems, circuits and devices

## Slide 3
Developing an electronic system
Systems
Material synthesis
Material processing
Material modeling
Transport study
Computation
Device design
Device modeling
Contacts
Simulation
Devices
Interconnects
Components
Integrated circuits (IC)
Material
Device/Circuit
Circuit/System

## Slide 4
Metal-oxide-semiconductor field effect transistors (MOSFETs)
The workhorse of modern electronic gadgets

## Slide 5
Si based CMOS is the key
Microelectronic market
80% is dominated by CMOS**
97% is covered by Si
Market
Si is abundant in nature
High quality native oxide (SiO2)
Appropriate mechanical strength
As a material
P - Metal-Oxide-Semiconductor Field Effect Transistor (p-MOSFET).
N - Metal-Oxide-Semiconductor Field Effect Transistor (n-MOSFET).
Complementary-Metal-oxide-Semiconductor (CMOS).
CMOS is a combination of an n-MOSFET and p-MOSFET.

## Slide 6
MOSFET
Vertical Electric Field
Lateral Electric Field
P-Substrate
Back contact
Oxide
Gate
- - - - - - - - - - -
Source
Drain
Channel
MOS
FET
Two orthogonal electric fields work together to initiate the operation of a MOSFET. Vertical field applied from the gate creates a channel for the carriers and lateral electric field drags the carriers from source to the drain, leading to generate a current along the channel.

## Slide 7
MOSFET schematics
P-Sub
N++
N++
n-MOS
p-MOS
Symbol
p-MOS
Symbol:
n-MOS

## Slide 8
Schematic:
SiO2
Poly-Si gate
Silicide
Si-substrate
Junctions
channel
D
S
G
VDS
Vgs
3 or 4-terminal devices:
Gate (G), Source (S) and Drain (D).
Import regions: channel, junctions, gate insulator.
Device parameters: Gate length (L), device width (W), oxide thickness, channel doping.
On application of voltages at the gate (VG), and S/D regions (VDS), current flows through the channel (from S to D).
MOSFET schematics
N_sub
N_channel
N_S/D

## Slide 9
Basic processing modules
Cleaning, Etching & Lithography
Annealing
Metallization
Silicidation
Deposition
Implantation
Oxidation
Activation
Diffusion

## Slide 10
Typical MOSFET process flow
HDD implant and activation
Ti deposition and SALICIDATION
Back end process & contact creation
Thermal gate oxidation
Poly-Si deposition and gate definition
LDD implant and activation
Si3Ni4 deposition & RIE
Main features:
Gate oxidation: ~ 800 C;
Dopant activation: 1000 C;
Side nitride spacer wall:
Anisotropic dry etching;
Silicide module: 800 C.

## Slide 11
Junction depth (Xj) and doping profile
Implantation
Implantation dose
Implantation energy
Implantation profile
Process parameters:
poly-Si
n+
n+
Junction depth: Xj
n+
Depth (nm)
Doping concentration (cm-3)
p=1016 (cm-3)
n=1020 (cm-3)
Xj
At the depth of Xj, the n-type (S/D) and p-type (substrate) doping concentrations will be same.
Low implant energy reduces junction depth, high energy increases it.

## Slide 12
Dimension: Lg, Tox and W
Oxide thickness: TOX
poly-Si
Channel length: L
n+
n+
Channel width: W
Process parameters:
Lithography
Wavelength used
Different techniques
Exposure time
Lateral diffusion of dopants
Physical and electrical length
Process parameters:
Oxidation time
Oxidation temperature
Oxidation environment
Oxidation techniques
Oxidation kinetics

## Slide 13
Physics of the metal-oxide-semiconductor (MOS) systems

## Slide 14
x
x1
xn
x3
………
..
Potential
Energy
S
M
O
Ψs
Band diagram of MOS system
Band bends on application of a gate voltage, leading to redistribution of carrier underneath the oxide layer.
Either the majority carrier or minority carriers will be attracted, depending upon the polarity of the applied voltage and substrate doping nature.
The measurement parameter is the surface potential (s).
Surface potential is positive when band bend downward and it is negative when it bend upward.

## Slide 15
3-D band alignment in a MOSEFT
Ψs
x1
xn
x3
………
..
Potential
Energy
Ψs
Gate
Source
Final surface potential is controlled by the simultaneous action of both the gate-to-channel and source-to-drain voltages.

## Slide 16
3-D band alignment in a MOSEFT
Gate
Substrate
Inversion layer
Depletion layer
Bulk region
B
B
S
S B
Source
Drain

## Slide 17
3-D band alignment in a MOSEFT
Inversion layer is tapered @ drain end. EFn crosses down to Ei near the drain.
Vg > Vth
EFp
Ei
Energy band configuration at Vg > Vth and Vd > 0.
3D
Vs = 0
Vd = 0
Ei
S
D
Vs = 0
Vd > 0
Ei
Inversion
Depletion
EFn
Ei

## Slide 18
MOSFET: transport modeling
Charge sheet model:
- channel is very thin, no voltage drops across it.
- vertical electric field is very high compared to lateral electric field.
- total charge at the metal side = to the net charge in the semiconductor side.
Net charge:
Current-voltage characteristic:
S
D

## Slide 19
Electrical characteristics
Transfer characteristics
0
VG
0.5 VG
ID
VD
0
VG
0.5 VG
Log (ID)
VD
Output characteristics
VD
0
0.5 VDD
ID
Linear region
Vg1
Vg4
Vg2
Vg3
Linear region:
Saturation region:

## Slide 20
Threshold voltage: Vth
Off-state leakage current: Ioff
On-state current: Ion
On-state/off-state current: Ion/Ioff
Trans-conductance: gm
Channel conductance: gd
Sub-threshold slope: S
Drain voltage: Vdd
Channel mobility: µ
S/D resistance: Rs and Rd
DIBL
Characteristic parameters